## Slide 1: What is an OPC UA?
OPC UA is a data exchange standard for industrial communication (machine-to-machine or PC-to-machine communication).
Open Platform Communications Unified Architecture

## Slide 2: OPC Foundation
The OPC Foundation is the organization behind the standard and with 678 members it has very broad base.
Its members include global players in the automation industry. For example: Siemens, Honeywell, Microsoft, Beckhoff, SAP, Yokogawa, ABB, Rockwell, Schneider Electric, Wago, Iconics and others.

## Slide 3: Industry 4.0
Industry 4.0 is the latest evolution of manufacturing.
It refers to the transformation of industry through the intelligent networking of machines and processes with the help of information and communication technology (ICT).
Different kinds of sensors gives the opportunity for making of smart factories where every machine action is traced.

## Slide 4: W hat is a PLC?
Programmable Logic Controller (PLC) is simply a special industrial computer that is programmed to control certain processes in industries like petroleum, steel or automotive industry. It contains three main parts: Input Module, CPU and Output Module.
There is also a programming computer, on which is written the program that will execute (and control) on PLC. When the program is written, it has to be uploaded to the PLC.

## Slide 5: What is an HMI?
A Human-Machine Interface (HMI) is a user interface or dashboard that connects an operator to controller for an industrial system (for example PLC) .
In industrial the HMI can be used for: Visual display of data, Track production time, Monitor machine inputs and outputs, oversee KPIs, etc.

## Slide 6: HMI in real environment

## Slide 7: What was before OPC? Driver diversity problem!
GIC driver
EATON driver
Siemens driver
HMI system
EATON PLC
Siemens PLC
  GIC PLC

## Slide 8: Classic OPC
OPC Server
HMI system (OPC client)
  GIC PLC
EATON PLC
Siemens PLC
Windows PC
COM/DCOM

## Slide 9: Classic OPC
The communication is based on COM and DCOM which are Microsoft technologies.
It works only on Windows machines and has not so rich features like OPC UA.
OPC is a software interface standard that allows Windows programs to communicate with industrial hardware devices.

## Slide 10: OPC UA
OPC UA first release is in 2008.
It has many more features than the old OPC.
It is platform independent and not only for Windows.
It has built in security and is Internet friendly oriented (No Firewall problems).
It is designed for work in Internet and specially for Industry 4.0.
It relies on TCP/IP protocol stack and uses Https and OPC binary protocol.
OPC UA
Platform Independence
Firewall friend

## Slide 11: OPC UA
OPC Server
HMI system (OPC client)
  GIC PLC
Eaton PLC
Siemens PLC

## Slide 12
Where is used OPC UA?
OPC UA

## Slide 13: OEE (Overall Equipment Effectiveness)
It’s a gold standard for measuring manufacturing productivity.
By measuring of OEE and the underlying losses, we can get important insights on how to systematically improve our manufacturing process.

## Slide 14: OPC UA Specifications
Information model
Communication architectures
Security
Historical access
Alarms and Events
Programs
"ns=2;s=/FloorOne/Machines/Pump"

## Slide 15: Communication architectures
Pub/Sub model (notifications)
Client/Server model (session)
session
client
server
server
client
client
client
client

## Slide 16: Hirschman project
client
client
server
read
write
read
write
subscriber
publisher

## Slide 17: Komax Connect Project
We already have an initial connection between CS WIN and the cloud KOMAX system.
For this purpose was developed CS WIN COM object which serves as a OPC UA client and OPC UA server which is a Windows service app that running on the same PC.

## Slide 18: KOMAX Connect Project
OPC UA server (Win service)
CS WIN
(OPC UA client
– COM object)
KOMAX Gateway
Cloud dashboard
write data
read data
OPC UA
OPC UA

## Slide 19: View from Komax Connect client in CS WIN