## Slide 1: OPC UA
OPC Unified Architecture and Industry 4.0

## Slide 2: Table of contents
What is an OPC UA?
Initial OPC project
Release of OPC UA
Where is used OPC UA?
Industry 4.0
OEE (Overall Equipment Effectiveness)
Smart manufacture
OPC UA protocols
OPC UA specifications
Traeger library C#
SDKs
Hirschman project demo
Komax Connect project demo

## Slide 3: What is an OPC UA?
OPC UA is a data exchange standard for industrial communication (machine-to-machine or PC-to-machine communication).
Open Platform Communications Unified Architecture

## Slide 4: Initial OPC project
OPC UA is a successor of older OPC that was created in 1996 by OPC Foundation.
The communication is based on COM and DCOM which are Microsoft technologies.
It works only on Windows machines and has not so rich features like OPC UA.

## Slide 5: Release of OPC UA
OPC UA first release is in 2008.
It has many more features than the old OPC.
It is platform independent and not only for Windows.
It has built in security and is Internet friendly oriented (No Firewall problems).
It is designed for work in Internet and specially for Industry 4.0.
It relies on TCP/IP protocol stack and uses Https and OPC binary protocol.
OPC UA
Platform Independence
Firewall friend

## Slide 6
Where is used OPC UA?
OPC UA

## Slide 7: Industry 4.0
Industry 4.0 is the latest evolution of manufacturing.
It refers to the transformation of industry through the intelligent networking of machines and processes with the help of information and communication technology (ICT).
Different kinds of sensors gives the opportunity for making of smart factories where every machine action is traced.

## Slide 8: OEE (Overall Equipment Effectiveness)
It’s a gold standard for measuring manufacturing productivity.
By measuring of OEE and the underlying losses, we can get important insights on how to systematically improve our manufacturing process.

## Slide 9: Smart manufacture

## Slide 10: OPC UA protocols
OPC UA Binary
HTTPS with UA Binary encoded attachment
HTTPS/SOAP with XML encoded messages

## Slide 11: OPC UA Specifications
Information model
Communication architectures
Security
Historical access
Alarms and Events
Programs
"ns=2;s=/FloorOne/Machines/Pump"

## Slide 12: Communication architectures
Pub/Sub model (notifications)
Client/Server model (session)
session
client
server
server
client
client
client
client

## Slide 13: OPC UA simple workflow

## Slide 14: OPC Classic to OPC UA communication
OPC Classic and OPC UA devices/software cannot communicated directly.
The integration of the new OPC UA technologies in the existing manufactories is not so easy and have to be done step by step.

## Slide 15: Traeger SDK (demo)
https://opcua.traeger.de/en/

## Slide 16: SDKs
Helpful links:
https://www.unified-automation.com/products/server-sdk/c-ua-server-sdk.html
https://open62541.org/
https://industrial.softing.com/products/opc-ua-and-opc-classic-sdks.html

## Slide 17: Hirschman project (demo)
client
client
server
read
write
read
write
subscriber
publisher

## Slide 18: Komax Connect Project
We already have an initial connection between CS WIN and the cloud KOMAX system.
For this purpose were developed CS WIN COM object which serves as a OPC UA client and OPC UA server which is a Windows service app that running on the same PC.

## Slide 19: KOMAX Connect Project (demo)
OPC UA server (Win service)
CS WIN
(OPC UA client
– COM object)
KOMAX Gateway
Cloud dashboard
write data
read data
OPC UA
OPC UA

## Slide 20: Thank you
By: Velizar Gerasimov